## Slide 1: IIOT Training
Jan-2024 Rev.A

## Slide 2
Table of contents
Day1
Basic MIC IIOT Device
Day2
Modbus with HMI (GOT)
Day3
Arduino OOP(2)
Day4
Real time database
MQTT
Multitasking
Modbus
Arduino OOP (1)

## Slide 3
Basic MIC IIOT Device(1)
MIC SMM002 Interface
Input interface
RS232
LAN
Output interface
MIC-SMM002
RS232
Communication
protocol
HMI GOT 2000
Modbus protocol
Diagram

## Slide 4
Basic MIC IIOT Device(2)
  IoT Gateway Module designed for seamless connectivity and communication.
Application Features
  Operates on 5VDC -1A
Power Requirements:
  Powered by the ESP32-S2-wrover-i for efficient and versatile control.
Microcontroller:
  Equipped with Ethernet and RS232 ports for flexible communication options.
Communication Ports:
  Supports SD Card for expanded storage capacity. Includes 4MB SPI Flash and 2MB PSRAM for efficient data handling.
Memory Storage
  Utilizes WiFi with a bit rate of 150 Mbps at the 2.4 GHz frequency.
Wireless Connectivity
  Supports MQTT, ModbusTCP, and ModbusRTU for seamless integration with various systems
Communication Protocols
IIOT Device features

## Slide 5
MQTT(1)
MQTT Concept

## Slide 6
MQTT(2)
Arduino with MQTT
Library : PubSubClient
1.MQTT simple : https://drive.google.com/file/d/14ONiJswlLQkfvosV9_e0AGpCK5Qh3lGf/view?usp=drive_link
2.MQTT multi data : https://drive.google.com/file/d/1DHtyyoI58EQfIvn38ac2vvkxSERP5Jlh/view?usp=drive_link
Errors list for MQTT

## Slide 7
Multitasking
Arduino with Mutitasking
Code : https://drive.google.com/file/d/1aQ1BOtpQ70SqpBalbzuQP453ZleV1zRN/view?usp=drive_link
Concept:
Priority 5
Task A
Task B
Priority 4
Task A
Task B
Priority …
Task A
Task B
Priority 0
Task A
Task B
CPU0
CPU1
xTaskCreatePinnedToCore(fTaskFunction,TaskName,StackDepth, PassParam,TaskPriority,TaskHandle,CPU);

## Slide 8
Modbus
Modbus RTU
Concept diagram
Type | Start address
Output coils | 000001
Input contacts | 100001
Input registers | 300001
Holding registers | 400001
Code : https://drive.google.com/file/d/1Dp_vIMGP63b8P4RrQrNveA2kc2_HTmfo/view?usp=drive_link